## Slide 1: NEW METHOD FOR NATURAL FREQUENCY AND DAMPING RATIO DETERMINATION VIA BUMP ROAD EXCITATION
Student: Do Thai An – ID: 1652005
Instructor: Dr. Tran Huu Nhan
Date: April 2nd, 2022
GRADUATION THESIS
VIETNAM NATIONAL UNIVERSITY HO CHI MINH CITY
HO CHI MINH CITY UNIVERSITY OF TECHNOLOGY
FACULTY OF TRANSPORTATION ENGINEERING
DEPARTMENT OF AUTOMOTIVE AND ENGINE

## Slide 2: CONTENTS
INTRODUCTION
THEORETICAL BASIS
MODEL DESCRIPTIONS
CALCULATION FLOW
RESULTS AND DISSCUSSION
CONCLUSIONS AND FUTURE WORKS
1.1 Suspension system
1.2 Suspension components
1.3 Analysis factors
1.4 Thesis objective & limitation

## Slide 3: 1.1 Suspension system
Suspension system: Connects a vehicle to its wheels and allows relative motion
Function of suspension:
  Carry the car and its weight
  Maintain correct wheel alignment
  Control the vehicle’s direction of travel
  Keep the tires in contact with the road
  Reduce the effect of shock forces

## Slide 4: 1.2 Suspension components
Guiding elements:
  Control arms, links
  Struts
  Leaf springs
Force elements:
  Coil spring, torsion bar, air spring, leaf spring
  Anti-roll bar, anti-sway bar or stabilizer
  Damper
  Bushings, hydro-mounts
Tires
Notes: Coil springs, torsion bars, and leaf springs absorb additional load by compressing. Thus, the ride height depends on the loading condition. Air springs are rubber cylinders filled with compressed air

## Slide 5: 1.2 Suspension components
Elastic
Damping
Notes: Coil springs, torsion bars, and leaf springs absorb additional load by compressing. Thus, the ride height depends on the loading condition. Air springs are rubber cylinders filled with compressed air

## Slide 6: 1.3 Analysis factors
1. Stability and Comfort
  Compare between air spring and leaf spring
  Compare between different input road excitation

## Slide 7: 1.3 Analysis factors
2. Natural frequency and damping ratio determination via bump road excitation
=> new method for determination of natural frequency and damping ratio alternative to the old method (22TCN 336:2006)

## Slide 8: 1.4 Thesis objective & scope
Investigate the effects of leaf spring – air spring parameters and road profiles on ride comfort and stability.
Investigate the appropriate road profile ,apply it to 22TCN 336:2006 industrial standard
Use quarter-car 2 DOF models, take system parameters of Primas bus as basis.
Hypothesis: linear suspension system (constant spring stiffness) and non-linear suspension system (variability spring stiffness, constant damping coefficient), no seat suspension.
Scope: IRC and GB/T road profiles, vehicle speed (20 km/h) and input frequency range from 0 to 16 Hz, 70 PSI air spring pressure.

## Slide 9: CONTENTS
INTRODUCTION
THEORETICAL BASIS
MODEL DESCRIPTIONS
CALCULATION FLOW
RESULTS AND DISSCUSSION
CONCLUSIONS AND FUTURE WORKS
2.1 Suspension models
2.2 Natural frequency & damping ratio
2.3 IRC – GB/T road profile
2.4 Evaluation indexes
2.5 Natural frequency and damping ratio determination

## Slide 10: 2.1 Suspension models
Vertical motions
Rotational motions
Figure 2.1: Quarter-car models (2,3,1 DOF)
Figure 2.2: Model of car vibration in the horizontal plane, 4DOF
Figure 2.3: Model of car vibration in the vertical plane, 4DOF
Figure 2.4: Model of car vibration 7DOF
Notes: Study vertical movement
Study vertical/pitch/roll movements

## Slide 11: 2.2 Natural frequency & damping ratio
Natural Frequency:
  For comfortable, the natural frequency usually fluctuates in the range of 1 – 1.5 Hz
Damping Ratio:
  For comfortable, the damping ratio usually fluctuates in the range of 0.2 – 0.4
Figure 2.5: Effect of natural frequency
Figure 2.6: Effect of damping ratio
Notes: Để dễ cho việc nghiên cứu, ta sẽ suy hết về dạng fn và zeta thay vì độ cứng và damping coefficient

## Slide 12: 2.3 IRC – GB-T road profile
IRC – Indian Road Congress
GB/T - standard GB/T 4970-2009, China

## Slide 13: 2.4 Evaluation indexes
Name | Symbol | Equation | Unit
Natural frequency |  |  | Hz
Damping ratio |  |  | 1
Body Vibration Acceleration |  |  | 
Suspension Dynamic Deflection |  |  | m
Tire relative Dynamic Load |  |  | N
Gain Response | Gain |  | 1
Name | Symbol | Equation | Unit
Natural frequency |  |  | Hz
Damping ratio |  |  | 1
Body Vibration Acceleration |  |  | 
Suspension Dynamic Deflection |  |  | m
Tire relative Dynamic Load |  |  | N
Gain Response | Gain |  | 1

## Slide 14: 2.5 Natural frequency and damping ratio determination
22TCN 336:2006 Standard method: (Minister of Transport)
  Create vertical oscillation
    Press down a half of car
    Lift a half of car
  Record the received oscillation signal
    Body acceleration signal
    Body displacement signal
  Processing test results
Dangerous while testing
Complicated
Costs for testing components
Drawbacks

## Slide 15: 2.5 Natural frequency and damping ratio determination
b) Proposal method
  Let the car run with the constant speed an in full load state through a proposal bump
  Record the received oscillation signal
    Body acceleration signal
    Body displacement signal
  Processing test results using above record signal
    Natural frequency
    Damping ratio

## Slide 16: CONTENTS
INTRODUCTION
THEORETICAL BASIS
MODEL DESCRIPTIONS
CALCULATION FLOW
RESULTS AND DISSCUSSION
CONCLUSIONS AND FUTURE WORKS
3.1 Models
3.2 Air spring parameters
3.3 Road parameters
3.4 Model parameters

## Slide 17: 3.1 Models

## Slide 18: 3.1 Models
Symbol | Unit | Description
 | kg | Sprung mass
 | kg | Un-sprung mass
 | N/m | Air-spring stiffness
 | N/m | Un-sprung stiffness
 | Ns/m | Sprung damping
 | m | Car body displacement
 | m | Un-sprung displacement
 | m/s | Car body velocity
 | m/s | Un-sprung velocity
y | m | Road excitation
Symbol | Unit | Description
 | kg | Sprung mass
 | kg | Un-sprung mass
 | N/m | Air-spring stiffness
 | N/m | Un-sprung stiffness
 | Ns/m | Sprung damping
 | m | Car body displacement
 | m | Un-sprung displacement
 | m/s | Car body velocity
 | m/s | Un-sprung velocity
y | m | Road excitation
ODE Equation:

## Slide 19: 3.2 Air spring parameters
Air spring 1R11-028 – GoodYear product

## Slide 20: 3.2 Air spring parameters
Name | Symbol | Value | Unit
Sprung weight |  | 2000 | kg
Air spring pressure | P | 70 | PSI
Linear stiffness |  | 103147.81 | N/m
Design height |  | 0.1945 | m
Suspension travel |  | 0.2413 | m
Extended travel |  | 0.1357 | m
Compressed travel |  | 0.1056 | m
Name | Symbol | Value | Unit
Sprung weight |  | 2000 | kg
Air spring pressure | P | 70 | PSI
Linear stiffness |  | 103147.81 | N/m
Design height |  | 0.1945 | m
Suspension travel |  | 0.2413 | m
Extended travel |  | 0.1357 | m
Compressed travel |  | 0.1056 | m

## Slide 21: 3.3 Road parameters
IRC Road
Name | Symbol | Value | Unit
Length |  | 5 | m
Height |  | 0.1 | m
Name | Symbol | Value | Unit
Length |  | 5 | m
Height |  | 0.1 | m
GB/T Road
Name | Symbol | Value | Unit
Length |  | 0.4 | m
Height |  | 0.04 | m
Name | Symbol | Value | Unit
Length |  | 0.4 | m
Height |  | 0.04 | m

## Slide 22: 3.4 Model parameters
Name | Symbol | Value | Unit
Sprung weight |  | 2000 | kg
Air spring pressure | P | 70 | PSI
Air spring design height |  | 0.1945 | m
 |  | 2000 | kg
Un-sprung mass (air spring) |  | 200 | kg
Un-sprung mass (leaf spring) |  | 250 | kg
Leaf-Air spring stiffness (linear) |  | 103147.81 | N/m
Un-sprung stiffness |  | 870000 | N/m
Sprung damping coefficient |  | 9000 | Ns/m
Vehicle speed | v | 20 | km/h
Name | Symbol | Value | Unit
Sprung weight |  | 2000 | kg
Air spring pressure | P | 70 | PSI
Air spring design height |  | 0.1945 | m
 |  | 2000 | kg
Un-sprung mass (air spring) |  | 200 | kg
Un-sprung mass (leaf spring) |  | 250 | kg
Leaf-Air spring stiffness (linear) |  | 103147.81 | N/m
Un-sprung stiffness |  | 870000 | N/m
Sprung damping coefficient |  | 9000 | Ns/m
Vehicle speed | v | 20 | km/h

## Slide 23: CONTENTS
INTRODUCTION
THEORETICAL BASIS
MODEL DESCRIPTIONS
CALCULATION FLOW
RESULTS AND DISSCUSSION
CONCLUSIONS AND FUTURE WORKS

## Slide 24: 4. CALCULATION FLOW
Input IRC road profiles
System parameters
Input GB/T road profiles
Time response calculation (ODE45 solver)
Compare stability characteristics
Time response calculation (ODE45 solver)
Frequency response
Frequency response
Evaluate
Conclusion
Evaluate the proposal road testing
passed
Input proposal road profiles
Time response calculation (ODE45 solver)
failed

## Slide 25: CONTENTS
INTRODUCTION
THEORETICAL BASIS
MODEL DESCRIPTION
CALCULATION FLOW
RESULTS AND DISSCUSSION
CONCLUSIONS AND FUTURE WORKS
5.1 Time response results
5.2 Frequency response results
5.3 Natural frequency and Damping ratio determination

## Slide 26: 5.1 Time response results

## Slide 27: 5.2 Frequency response results

## Slide 28: 5.2 Frequency response results

## Slide 29: 5.3 Natural frequency and Damping ratio determination

## Slide 30: 5.3 Natural frequency and Damping ratio determination

## Slide 31: 6. CONCLUSIONS
50% progress
Change topic’s name to “DYNAMIC ANALYSIS OF THE PRIMAS BUS USING 2DOF MODEL WITH AIR SPRING AND RESEARCH NEW METHOD FOR NATURAL FREQUENCY AND DAMPING RATIO DETERMINATION VIA BUMP ROAD EXCITATION”

## Slide 32: THANK YOU FOR LISTENING

## Slide 35: CONTENTS
INTRODUCTION
THEORETICAL BASIS
MODEL DESCRIPTIONS
CALCULATION FLOW
RESULTS AND DISSCUSSION
CONCLUSIONS AND FUTURE WORKS

## Slide 38
Conclusion
Ride comfort of T880 truck satisfy comfort requirement on road class A and B under all load cases
Natural frequency increase -> ride comfort decrease
Damping ratio increase -> ride comfort decrease
Calculation results can be used as basis to determine system parameters of suspension in designing process
Future works
Conduct experimental investigation
=> Compare difference between theoretical and practical situations
Modelization of non-linear spring and damper
=> Compare performance between different types of suspension system (air spring, skyhook damper)
Study relationship between ride comfort and handling
=> Utilize 3D model to study rotational motions
6. CONCLUSIONS

## Slide 41: 3.3 Road parameters
Figure 3.1: Non-linear model
Figure 3.2: Linear model
Suspension system
Sprung weight
Tire modelization
Un-sprung weight
Air spring
Leaf spring

## Slide 44: 1. INTRODUCTION

## Slide 45: 2. THEORETICAL BASIS

## Slide 46: 3. MODEL DESCRIPTIONS

## Slide 47: 4. CALCULATION FLOW

## Slide 48: 5. CONCLUSION & FUTURE WORKS

## Slide 49: Tổng quan
Thể loại LVTN: Nghiên cứu mô phỏng
Mục tiêu nghiên cứu:
  Phương pháp: mô phỏng số trên mô hình 2dof spring mass damper
  Công cụ: MATLAB 2018
Thesis scope
Thesis objective
Research methodology
Những bài toán cần giải quyết

## Slide 50: Objective/Scope

## Slide 51: 2. INPUT

## Slide 52: 2.1. AIR SPRING INPUT
Air spring 1R11-028 – GoodYear product

## Slide 53: AIR SPRING Stiffness Calculating
Stiffness formular:

## Slide 54: Air spring calculating parameters
Name | Symbol | Value | Unit
Sprung weight |  | 2000 | kg
Air spring pressure | P | 70 | PSI
Linear stiffness |  | 103147.81 | N/m
Design height |  | 0.1945 | m
Suspension travel |  | 0.2413 | m
Extended travel |  | 0.1357 | m
Compressed travel |  | 0.1056 | m
Name | Symbol | Value | Unit
Sprung weight |  | 2000 | kg
Air spring pressure | P | 70 | PSI
Linear stiffness |  | 103147.81 | N/m
Design height |  | 0.1945 | m
Suspension travel |  | 0.2413 | m
Extended travel |  | 0.1357 | m
Compressed travel |  | 0.1056 | m

## Slide 55: IRC Road INPUT
IRC is the Indian Road profile Congress

## Slide 56: Standard GB/T 4970–2009 Road Input
The triangular bump model is created on the basis of the national standard GB/T 4970-2009, China

## Slide 57: Calculating model
2DOF spring mass damper model
Symbol | Unit | Description
 | kg | Sprung mass
 | kg | Un-sprung mass
 | N/m | Air-spring stiffness
 | N/m | Un-sprung stiffness
 | Ns/m | Sprung damping
 | m | Car body displacement
 | m | Un-sprung displacement
 | m/s | Car body velocity
 | m/s | Un-sprung velocity
Symbol | Unit | Description
 | kg | Sprung mass
 | kg | Un-sprung mass
 | N/m | Air-spring stiffness
 | N/m | Un-sprung stiffness
 | Ns/m | Sprung damping
 | m | Car body displacement
 | m | Un-sprung displacement
 | m/s | Car body velocity
 | m/s | Un-sprung velocity

## Slide 58: Input Parameters
Name | Symbol | Value | Unit
Sprung weight |  | 2000 | kg
Air spring pressure | P | 70 | PSI
Design height |  | 0.1945 | m
 |  | 2000 | kg
Un-sprung mass air spring |  | 200 | kg
Un-sprung mass leaf spring |  | 250 | kg
Leaf-air spring stiffness |  | 103147.81 | N/m
Un-sprung stiffness |  | 870000 | N/m
Sprung damping |  | 9000 | Ns/m
Name | Symbol | Value | Unit
Sprung weight |  | 2000 | kg
Air spring pressure | P | 70 | PSI
Design height |  | 0.1945 | m
 |  | 2000 | kg
Un-sprung mass air spring |  | 200 | kg
Un-sprung mass leaf spring |  | 250 | kg
Leaf-air spring stiffness |  | 103147.81 | N/m
Un-sprung stiffness |  | 870000 | N/m
Sprung damping |  | 9000 | Ns/m

## Slide 59: Calculating and result
Name | Symbol | Value | Unit
IRC Road height | h | 0.1 | m
Air spring pressure | P | 70 | PSI
Design height |  | 0.1945 | m
 |  | 2000 | kg
Un-sprung mass air spring |  | 200 | kg
Un-sprung mass leaf spring |  | 250 | kg
Leaf-air spring stiffness |  | 103147.81 | N/m
Un-sprung stiffness |  | 870000 | N/m
Sprung damping |  | 9000 | Ns/m
Name | Symbol | Value | Unit
IRC Road height | h | 0.1 | m
Air spring pressure | P | 70 | PSI
Design height |  | 0.1945 | m
 |  | 2000 | kg
Un-sprung mass air spring |  | 200 | kg
Un-sprung mass leaf spring |  | 250 | kg
Leaf-air spring stiffness |  | 103147.81 | N/m
Un-sprung stiffness |  | 870000 | N/m
Sprung damping |  | 9000 | Ns/m

## Slide 60: 3. Calculating and results

## Slide 61: 3.1. Compare IRC – GB/T
Name | Symbol | Value | Unit
IRC Length | L | 0.1 | m
IRC Height | h | 5 | m
GB/T Length | L | 0.4 | m
GB/T Height | h | 0.04 | m

## Slide 62: 3.1.1. IRC – GB/T Time response result